SEP: Board decision

On 25/07/2020, Quang Tri general trading joint stock company announced board decision as follows:

Article 1: Approve the project on purchasing cassava starch production line as follows:

- Name of project: Purchasing cassava starch production line

- Investor: Quang Tri general trading joint stock company

- Capacity: 60 tons/ day and be able to be upgraded to 120 tons in the future

- Purpose:

- Purchasing the cassava starch production line with the modest technology to meet the demand of domestic and foreign market.

- Gradually replacing the current production line, which has been declining due to being used in 20 years.

- Maintaining the production capacity of the entire line at 270 tons/day and increase the recovery rate

- Taking advantages of the large source of materials in the area and a team of professional technical staff

- Investment location:

- At Huong Hoa cassava starch Factory, Thuan commune, Huong Hoa district

- Contents and investment scale:

- Purchasing additionally 01 production line, house and warehouse next to the old factory with total area: Width 16.5m x Length 88m, built with prefabricated steel

- Main machinery and equipment are imported, other equipment will be processed domestically to unify with the current production line and the general production ground of the Factory

- Upgrading the capacity of residue drying line up to 20 tons/day

- Expanding the road to new position parallel to drainage ditch

- Dig 01 additional biogas lake covered with canvas, size: 60m x 120m x 5m = 36,000 m3, which is adjacent to the biogas lake No. 02. The wastewater will be distributed into 02 sources: 1. Biogas lake No. 1, 2. New biogas lake; water from these 02 lakes shall return to biogas lake No. 2 then biogas lake No. 3 as current.

- Total investment:

- Equipment cost:				VND 32,822,413,000

- Construction cost: 			VND 13,090,818,000

- Project management cost: 		VND 1,183,183,962

- Construction consulting cost:		VND 2,011,847,720

- Other cost:				VND 494,146,046

- Reserve cost:				VND 2,455,413,134

Total: 					VND 52,057,821,862

TOTAL (ROUNDED):			VND 52,057,822,000

- Source: Equity and bank loan

- Management method: Managed directly by Investor

- Implementation time: From 24/07/2020 to 31/12/2020

- Date of starting operations: 31/12/2020

Article 2: This decision took effect from the date of signature